## Slide 1: ICAO FLIGHT PLAN
FAA domestic guidance
Updated: 11/18/2016(Ching-Kuan Su)

## Slide 2: Why do we need to learn it?
FAA will start to use the ICAO flight plan Form in January, 2017
Match ICAO Standard
The ICAO flight plan form will give ATC more details on your aircraft equipment.

## Slide 3: Understand your aircraft equipment
Navigation equipment:
  GPS/VOR/DME/IRU/LORAN/ADF/TACAN/LOC/ILS/MLS…etc.
Communication Equipment:
  VHF/UHF/HF/CPDLC(satellite phone)…etc.
Surveillance Equipment:
  Transponder/ADS-B…etc.
Survival equipment:
  ELT/Survival equipment/Lift Jacket…etc.
Others

## Slide 4: Where can you find the equipment info.?
POH/AFM
System Status Page for software version
  Consult with your CFI or AMT if you do not know how to find the info.
Manufacturer

## Slide 5: What should I put in equipment code?
We only put the equipment code which meets the following ICAO flight plan criteria.
  Presence of relevant serviceable equipment on board the aircraft;
  Equipment and capabilities commensurate with flight crew qualifications; and
  Where applicable, authorization from the appropriate authority

## Slide 6: UD ICAO Equipment codes

## Slide 7: Appendix I-GPS term.
FAA
GPS(Global Positioning System)
LAAS(Local Area Augmentation System)
  GLS(GBAS Landing System)
WAAS(Wide Area Augmentation System)
ICAO
GNSS(Global Navigation Satellite System)
GBAS(Ground Based Augmentation System)
SBAS(Satellite Based Augmentation System)

## Slide 8: Appendix II-GPS equipment
TSO-C129/TSO-C196: GPS without WAAS
TSO-C145/C146: GPS with WAAS
RAIM(Receiver Autonomous Integrity Monitoring)
FDE(Fault detection and exclusion)